## Slide 1: Protection & monitoring systems
  Presenter:
Title:
Date:

## Slide 2
Advanced systems for machinery protection and condition monitoring specially designed for critical rotating machinery within the power generation, oil & gas, and process industries.

## Slide 3: Product lines overview
  Advanced machinery protection and condition monitoring software
Software Solutions
  Protection and monitoring system hardware for critical rotating machinery
Protection & Monitoring Systems
Sensing solutions to monitor critical plant and equipment
Sensors & Conditioners

## Slide 4
Portfolio overview

## Slide 5
Overspeed detection and protection
PORTFOLIO OVERVIEW Advanced machinery protection, condition and performance monitoring for high-value rotating machinery
Protection and/or condition monitoring
VM600Mk2 Centralized rack-based advanced machinery protection and condition monitoring system. Suitable for applications with a medium-to-high channel count.
* Standard rack heights of 6U and 1U.
VibroSmart® Distributed module-based scalable system suitable for applications with a low-to medium channel count.
SpeedSys300 Scalable, robust and independent layer of protection to deliver fast and reliable protection against overspeed.
Notes: Product line logic
Add real examples of application (number of VM600 installed etc)

## Slide 6: Vm600Mk2/ VM600 Rack-based systems For machinery Protection and/or condition monitoring

## Slide 7: VM600Mk2/ VM600 racks
19″ system racks (ABE04x) with a standard height of 6U
Note: Space (rack slots) for up to 12 processing modules, such as MPC4Mk2 + IOC4Mk2.
19″ slimline rack (ABE056) with a standard height of 1U
Note: Space (rack slot) for 1 processing module, such as MPC4Mk2 + IOC4Mk2.

## Slide 8: DESIGN CONCEPT
VM600Mk2
Centralized system – designed to centrally process a wide range of different input signals coming from a variety of critical assets.
Flexible network architecture – easy integration with VibroSmart® distributed monitoring system for optimal and flexible network architecture in a condition monitoring system platform.
All measurements in one module – enables complex systems to be built with a minimum number of modules (modular structure with smart function combination).
MPC4Mk2 module supports machinery protection and condition monitoring
Industry standards
    API 670 compliant.
    Cybersecurity in accordance with IEC 62443.
    SIL 2 in accordance with IEC 61508.

## Slide 9
VM600 success story
Over 8,000 VM600 racks installed worldwide with:
40,000 machinery protection modules (MPC4)
5,500 condition monitoring modules (/XMV16/XMC16/CMC16)
Our Legacy
20+ years of machinery monitoring success
VM600 was introduced to the market in 2001
Innovation drive: VM600Mk2 is our latest rack-based system for protection and condition monitoring (replacing the VM600)

## Slide 10: VM600Mk2 MPC4Mk2 + IOC4Mk2
4 dynamic channels + 2 auxiliary channels (configurable as tacho or DC)
Up to 10 processed outputs per channel
4 user-configurable relays + 1 common circuit-fault relay (module fault)
4 analog outputs (4 to 20 mA or 0 to 10 V)
6 BNC connectors for buffered “raw” outputs
2 front panel buttons for module lock/unlock, reboot and recovery
Diagnostics (built-in self-test (BIST)) provides continuous feedback on the health of the module
VM600Mk2 system safety-line to drive all system relays to a safe state
Ethernet (100 Mbps) for communication with VibroSight® software
Conforms to API 670
VME bus communications with CPUMMk2
VM600Mk2 machinery protection and condition monitoring module

## Slide 11: New approach with enhanced monitoring capabilities
VM600Mk2 MPC4Mk2 + IOC4Mk2 module supports both machinery protection (MPS) and condition monitoring (CMS) – MPC4Mk2 CMS requires a license!
VibroSight Protect for MPC4Mk2 machinery protection (MPS) functionality / VibroSight Capture for MPC4Mk2 condition monitoring (CMS) functionality
Visibility of relay status, protection alarms and processing results from the monitoring software
Using separate software modules for the configuration and operation of MPC4Mk2 functionality/systems helps ensure complete separation (“segregation”) of MPS and CMS in a single VM600Mk2/ VM600 rack.
Change of MPC4Mk2 machinery protection requires physical access to the VM600Mk2 rack => cybersecure
VM600Mk2/ VM600 machinery protection and condition monitoring solutions
XMV16
MPC4Mk2
VibroSight ® condition monitoring software
VM600 rack
Machinery protection
Condition monitoring
Ethernet communications link
Sensors / measurement chains
VibroSight ® machinery protection software
(Permanent)
(Temporary)

## Slide 12: New approach with enhanced monitoring capabilities
VM600Mk2/ VM600 XMx16 + XIO16T modules support condition monitoring only (XMV16 for vibration, XMC16 for combustion)
VibroSight Configurator to configure XMx16 condition monitoring
Other VibroSight software modules are used for the operation and management of VM600Mk2/ VM600 modules/systems in the usual way. For example, VibroSight Vision for data display and analysis, VibroSight System Manager to configure hardware (IP addresses), update firmware, manage licensing, etc.
VM600Mk2/ VM600 machinery protection and condition monitoring solutions
XMV16
MPC4Mk2
VibroSight ® condition monitoring software
VM600 rack
Machinery protection
Condition monitoring
Permanent Ethernet communications link
Sensors / measurement chains
VibroSight ® machinery protection software

## Slide 13: VM600Mk2 MPC4Mk2 comparison against MPC4 (Mk1)
Feature / specification | VM600Mk2 MPC4Mk2 | VM600 MPC4
Analog to digital converter (ADC) resolution | 24 bit | 12 bit
Frequency bandwidth | 20 kHz | 10 kHz
Measurement outputs per channel | Up to 10 | Up to 2
Waveforms and spectra for troubleshooting | Yes | No
Epoxy sealed relays with all contacts (COM, NC, NO) available | Yes (4 + 1) | No (4)
Software configurable relays (normally energized (NE) or normally de-energized (NDE) – without jumpers) | Yes | No
System safety-line to drive relays to a safe state | Yes | No
Physical module lock for cybersecurity | Yes | No
Condition monitoring | Yes | No
SIL 2 | Yes “by design” (2022) | Yes “proven in use”
VM600Mk2 MPC4Mk2 + IOC4Mk2 module

## Slide 14: Single-channel processing
VibroSight Protect software |  | VM600 MPSx software (equivalent)
Bearing absolute vibration |  | (BBAB) Broad Band Absolute Bearing Vibration
Bearing absolute vibration or Shaft relative vibration |  | (NB) Narrow Band (Tracking) Vibration
Shaft relative vibration |  | (RS) Relative Shaft Vibration
Position Shaft axial position (collar) Shaft axial position (shaft end) | Rotor position (collar) Differential expansion (collar) Rotor expansion (collar) | (PS) Position
Shaft eccentricity |  | (EC) Eccentricity
Housing expansion |  | (HE) Absolute Housing Expansion
Differential expansion (pendulum) |  | (SEP) Relative Shaft Expansion With Pendulum
Broad band pressure |  | (BBP) Broad Band Pressure
Quasi-static pressure |  | (QSP) Quasi-static Pressure
Quasi-static temperature |  | (QST) Quasi-static Temperature
Bearing absolute vibration or Shaft relative vibration |  | (NBFS) Narrow Band Fixed Frequency
Speed |  | Speed
VM600Mk2 MPC4Mk2 + IOC4Mk2 module

## Slide 15: Dual-channel processing
VibroSight Protect software | VM600 MPSx software (equivalent)
X-Y shaft relative vibration | (SMAX) Smax
Differential housing expansion | (DHE) Differential Housing Expansion
Differential expansion (single taper) Differential expansion (dual taper) | (RST) Relative Shaft Expansion (Shaft taper)
Shaft axial position (collar) Shaft axial position (shaft end) Differential expansion (collar) | (RSC) Relative Shaft Expansion (Shaft collar)
Mathematical function | (DMF) Dual Mathematical Function
Delta Quasi-static Pressure | (DQSP) Delta Quasi-static Pressure
Delta Quasi-static Temperature | (DQST) Delta Quasi-static Temperature
Shaft absolute vibration | (AS) Absolute Shaft Vibration
VM600Mk2 MPC4Mk2 + IOC4Mk2 module

## Slide 16: VM600Mk2 RLC16Mk2
VM600Mk2 relay module
Feature / specification | VM600Mk2 RLC16Mk2 | VM600 RLC16
Machinery protection relays (user configurable) | 16 | 16
Epoxy sealed relays with all contacts (COM, NC, NO) available | Yes | No
Software configurable relays (normally energized (NE) or normally de-energized (NDE) – without jumpers) | Yes | No
Module OK via Raw bus line (“Status”) | Yes | No
System safety-line to drive relays to a safe state (“Redline”) | Yes | No
SIL 2 | Yes “by design” (2022) | Yes “proven in use”

## Slide 17
CPUMMk2 + IOCNMk2
VM600Mk2 rack controller and communications interface module
VM600Mk2 module data aggregation, processing and sharing (VME bus communications with MPC4Mk2, XMx16)
Industry standard fieldbus communications interfaces: Modbus TCP and PROFIBUS DP
Mathematical operations on fieldbus data
System/module status (health) information available via fieldbus
Front-panel alarm reset (AR) button
VM600 rack (CPUMMk2) security with a removable key
Two system Ethernet connections and two fieldbus connections can run simultaneously
Communications redundancy with two fieldbuses: Ethernet and/or serial
Two relays to signal system status and alarm information

## Slide 18: VibroSight Protect
VibroSight ® software module designed and optimized specifically for operation with VM600Mk2
VibroSight Protect supports the configuration and operation of the machinery protection (MPS) functionality for a VM600Mk2 system: MPC4Mk2 + IOC4Mk2, RLC16Mk2, CPUMMk2 + IOCNMk2
New easy to use and intuitive user interface
Separate configuration (*.mpscfg file)
Fast configuration
Checks overall system (rack) configuration consistency (as opposed to one-by-one module configuration)
Machinery protection configuration software

## Slide 19: VibroSight Capture
VibroSight ® software module designed and optimized specifically for operation with VM600Mk2
VibroSight Capture supports the configuration and operation of the condition monitoring (CMS) functionality for a VM600Mk2 system: MPC4Mk2 + IOC4Mk2
New easy to use and intuitive user interface
Separate configuration (*.cmscfg file)
Fast configuration
Fully-integrated support for VibroSight database management (no external data/database management tools are required)
Condition monitoring configuration software

## Slide 20
VM600Mk2/VM600 XMV16 + XIO16T
VM600Mk2/ VM600 condition monitoring module for vibration
Vibration monitoring for critical and large industrial applications requiring higher-performance and/or larger channel counts
16 dynamic channels + 4 tacho (speed) channels, also configurable as DC
Individually configurable channels with simultaneous and seamless data acquisition (fixed frequency or order tracked)
Up to 20 processed outputs per channel
High-resolution spectra (FFT): up to 6400 lines every 500 ms, up to 3200 lines every 200 ms, up to 1600 lines every 100 ms
Multiple alarms per output with configurable limits, hysteresis and time delay
Gigabit Ethernet (1000 Mbps) for communication with VibroSight®
VME bus communications with CPUMMk2

## Slide 21
Optimised for combustion (and vibration) monitoring
Combustion: Specific FFT windows options / Proprietary algorithm included (OEM applications)
16 dynamic channels + 4 tacho (speed) channels, also configurable as DC
Individually configurable channels with simultaneous and seamless data acquisition (fixed frequency or order tracked)
Up to 20 processed outputs per channel (Combustion: Band-peak extraction for combustion monitoring)
High-resolution spectra (FFT): up to 6400 lines every 500 ms, up to 3200 lines every 200 ms, up to 1600 lines every 100 ms (Combustion: Data aggregation of internal spectra)
Multiple alarms per output with configurable limits, hysteresis and time delay
Gigabit Ethernet (1000 Mbps) for communication with VibroSight®
VME bus communications with CPUMMk2
VM600Mk2/VM600 XMC16 + XIO16T
VM600Mk2/ VM600 condition monitoring module for combustion

## Slide 22
Key features
User-friendly advanced vibration monitoring and analysis
Allows to efficiently handle large numbers of measurement points and extensive volumes of data
Easy correlation of data from different systems is supported in cybersecure environments
VibroSight software suite
VM600Mk2 condition monitoring system
Modular, flexible and comprehensive machinery protection and condition monitoring solutions for a wide range of applications within the power generation, oil & gas and process industries.

## Slide 23: VibroSmart ® Distributed monitoring system For machinery Protection and/or condition monitoring

## Slide 24: DESIGN CONCEPT
VibroSmart VSV30x
Distributed system
Modular and scalable system designed for condition monitoring and machinery protection applications of critical assets.
Flexible Highly scalable and easy to extend.
Wide range of applications From stand-alone module on balance of plant equipment, up to several connected units for larger critical rotating machinery.
Real-time communication Via Ethernet or fieldbus.
Lower installation costs Skid-mounting of modules closer to machinery reduces expensive cabling.
Industry standards
    API 670 fully compliant
    Cybersecurity certification per IEC 62443
    SIL 2
    ATEX-certified (Zone 2)

## Slide 25: SYSTEM FEATURES
VibroSmart VSV301 + VSB300
ATEX-certified (Zone 2)
Directly mounted to the machine (DIN-rail)
Measurement chain: suitable for accelerometers, proximity (eddy current) and velocity sensors.
VibroSight: compatible with vibro-meter’s analysis and data processing software
2 dynamic channels and 1 analog input
Auxiliary input channel for tachometer
4 basic and 2 advanced logic functions to drive the module’s relays
Ethernet communications

## Slide 26: SYSTEM FEATURES
VibroSmart VSI010 + VSB010
ATEX-certified (Zone 2)
Directly mounted to the machine
Fieldbus server (slave) device acting as a data bridge between the modules and fieldbus master devices
(third-party systems)
VibroSight: compatible with vibro-meter’s analysis and data processing software
Up to 2 fieldbus ports
8 basic and 4 advanced logic functions to combine alarm and status information to drive module’s relays
Communications interfaces for industry standard fieldbuses: Modbus RTU, Modbus TCP, PROFIBUS DP and
GOOSE (IEC 61850)

## Slide 27: SpeedSys300 Overspeed detection system

## Slide 29: Design concept
SpeedSys300 ODS301 is designed as an independent layer of protection; to be fundamentally simple and robust. It delivers fast and reliable protection for speed and acceleration, and complies to important industry standards such as SIL and ATEX.

## Slide 30: SpeedSys300 ODS301
Key features and benefits
Safety by design
Scalable
API 670 compliant
Advanced self-monitoring and diagnostics
SIL 2 and SIL 3 capable: certified “by design”
Proof-test interval (PTI): 10 years
Dedicated overspeed system (isolated layer or protection)
Fast response time
External voting logic
Modular design
Compatible with industry standard speed sensors
Ex certified input channel interfaces for use with sensors / measurement chains installed in hazardous areas

## Slide 31: SpeedSys300 ODS301
SpeedSys300 ODS301 features/specificatons | 
Sensor compatibility | Proximity (eddy current), electronic (Hall effect) or magnetic (variable reluctance) speed sensors / measurement chains
Signal processing | The ODS301 module counts measurement chain pulses and converts them to rotational speed and acceleration measurements, which are compared against configured alarm limits. Safety outputs are activated for critical alarms while non-safety outputs are used for other alarms/status information.
Frequency range | 0.025 Hz to 35 kHz
Response time | 10 ms (typical)
Safety outputs | 2 × double-pole single-throw (DPST) safety relays and 1 × analogue 4 to 20mA current loop – certified for SIL safety loops
Non-safety outputs | 2 × single-pole single-throw (SPST) relays, 1 × frequency (speed) output, 1 × binary (status) output and 1 × Modbus RTU serial interface (read only)
Diagnostics technology | Advanced self-monitoring and diagnostics (that is, built-in self-test (BIST)) monitors and reports the health/status of the complete system
Proof test interval (PTI) | 10 years (typical)
Specfications

## Slide 32: SIL 3 solutions – relays
SpeedSys300 ODS301
PCS/ACTUATOR
SPEED SIGNAL
SPEED SIGNAL
SPEED SIGNAL
PCS/ACTUATOR
SPEED SIGNAL
SPEED SIGNAL

## Slide 33: SIL 2 solutions – relays and analog output
SpeedSys300 ODS301
PCS/ACTUATOR
SPEED SIGNAL
SPEED SIGNAL
PCS/ACTUATOR
SPEED SIGNAL
PCS/ACTUATOR
SPEED SIGNAL

## Slide 34: SpeedSys300 ODS301
  Interface: 2-wire current signal (analogue)
  TQ9xx, EA90x and IQS900 proximity measurement chains – with optional diagnostics for SIL safety related applications more info here
  Wide speed range
  Operation up to 180°C
  Long distance signal transmission (up to 1 km – further than any other solution)
  Preferred solution for a wide range of applications
  Interface: 3-wire voltage signal (digital)
  Preferred for low rpm / zero speed applications
  Easily transmittable and processable digital output signal
  Less vulnerable to electromagnetic interference (EMI)
  Interface: 2-wire voltage signal (analogue)
  Preferred for high rpm applications
  Suitable for high temperature applications (300°C)
  Self-powered
  Proximity (eddy current)
  Electronic (Hall effect)
  Magnetic (variable reluctance)
Sensor input compatibility

## Slide 35: Thank you

## Slide 36: Disclaimer
Business legal entity, Business address
Legal entity registration information as appropriate
Information contained in this document may be subject to export control regulations of the United Kingdom, European Union, United States or other national jurisdictions, including the US International Traffic in Arms Regulations and/or Export Administration Regulations.
Each recipient of this document is responsible for ensuring that transfer or use of any information contained herein complies with all relevant Export Control Regulations.
Copyright © 2022 Meggitt SA. All rights reserved.