## Slide 1: Sensors & conditioners
  Presenter:
Title:
Date:
Sensors / measurement chains for turbomachinery & essential rotating equipment

## Slide 2
  Our comprehensive Sensors & Conditioners product portfolio includes complete measurement chains for absolute and relative vibrations such as acceleration, velocity, displacement or gap.
  We provide accurate, safe and reliable solutions for extreme environments and critical applications such as bearing and relative shaft vibration protection of rotating equipment, gas turbine online combustion tuning, generator air-gap monitoring, housing expansion, etc.

## Slide 3: Product lines overview
  Advanced machinery protection and condition monitoring software
Software Solutions
  Protection and monitoring system hardware for critical rotating machinery
Protection & Monitoring Systems
Sensing solutions to monitor critical plant and equipment
Sensors & Conditioners

## Slide 4
Portfolio overview

## Slide 5: Sensing solutions for harsh environments
Gas turbines
Combustion
(dynamic pressure sensors)
Displacement - Position - Speed
(proximity sensors)
Absolute vibration
(accelerometers)

## Slide 6: Sensing solutions
Hydro turbines
Absolute vibration
(accelerometers)
Displacement - Position - Speed
(proximity sensors)
Vibration as velocity
(velocity sensors)
Winding current
(partial discharge)
Rotor-stator gap
(air-gap sensors)

## Slide 7: Absolute vibration

## Slide 8: High-temperature piezoelectric accelerometers
Our piezoelectric-based accelerometers are designed for the long-term measurement and monitoring of absolute vibration in the most severe of environments
CA series
Key features and benefits | 
Safety standards | Ex certified Up to SIL 2 (using IPC707 signal conditioner)
Operating temperatures | Up to 700 °C for sensors and 85 °C for IPC707 signal conditioner
Sensitivities | From 10 to 100 pC/g
Measurement ranges | From 0.001 to 500 g (dynamic) Up to 1000 g (overload)
Frequency responses | From 0.5 to 10,000 Hz
Signal conditioner | IPC707 has optional diagnostics (built-in test equipment (BITE)), required for SIL 2. Uses external IPC707 signal conditioner.
Linearity (typical) Transverse sensitivity Sensitivity tolerance | ± 1 % < 5 % ± 5 %

## Slide 9: CA series overview
Signal conditioner
Galvanic separator
More than 10,000 CA sensors / measurement chains installed yearly by OEMs and end users worldwide

## Slide 10: Accelerometers and velocity sensors
With attached or integrated electronics
For applications that do not require the temperature capabilities of a CA series sensor, this series provides a more cost-effective and easier to install solution
Key features and benefits |  | 
 | With attached electronics | With integrated electronics
Safety standards | Ex certified | Ex certified
Operating temperatures | Up to 350 °C | Up to 140 °C
Sensitivities | From 5 to 50 μA/g | From 50 to 500 mV/g (CE6xx) From 4 mV/mm/s (PV660)
Measurement ranges | From 0.001 to 400 g (dynamic) Up to 2000 g (overload) | Up to 80 g (CE6xx) Up to 100 mm/s (PV6xx)
Frequency responses | From 2 to 10,000 Hz | From 2 to 10,000 Hz
Signal conditioning | Uses attached or integrated electronics. Note: No external signal conditioner, so no connectors close to the machinery being monitored and easier to install. | 

## Slide 11: Accelerometers overview
With attached or integrated electronics

## Slide 12: Velocity sensors overview
With attached or integrated electronics

## Slide 13: Dynamic pressure

## Slide 14
Our piezoelectric-based dynamic pressure sensors are designed for the long-term measurement and monitoring of combustion in gas turbines: combustor pulsations and combustion dynamics.
Key features and benefits | 
Safety standards | Ex certified Up to SIL 2 (using IPC707 signal conditioner)
Operating temperatures | Up to 700 °C for sensors and 85 °C for IPC707 signal conditioner
Sensitivities | From 25 to 750 pC/bar
Measurement ranges | From 0.00005 to 250 bar (dynamic) Up to 350 g (overload)
Frequency responses | From 2 to 15,000 Hz
Linearity (typical) | ±1%. Note: Low sensitivities to acceleration.
Signal conditioner | Uses external IPC707 signal conditioner. IPC707 has optional diagnostics (built-in test equipment (BITE)), required for SIL 2.
Piezoelectric dynamic pressure sensors
CP series

## Slide 15: CP series overview
Patented acceleration-compensated designs with the highest temperatures and pressure sensitivities in the industry

## Slide 16: Relative vibration

## Slide 17: Proximity measurement chains
Our eddy-current based sensors are designed for the contactless measurement of the relative displacement of moving machine elements
Key features and benefits | 
Safety standards | API 670 5th edition compliant Ex certified Up to SIL 2 (using IQS900 signal conditioner)
Operating temperatures | −40 to 180 °C for sensors and cabling −40 to 85 °C for signal conditioner
Measurement ranges | TQ9x1: 2 mm range with 8 mV/μm or 2.5 μA/μm sensitivity (Ø 5 mm tip) TQ9x2: 2 mm range with 8 mV/μm or 2.5 μA/μm sensitivity or 4 mm range with 4 mV/μm or 1.25 μA/μm sensitivity (Ø 8 mm tip) TQ9x3: 12 mm range with 1.33 mV/μm or 0.417 μA/μm sensitivity (Ø 18 mm tip)
Frequency response | DC to 20,000 Hz
Mounting | Standard, reverse or right-angle (90°) mounting
Pressure | Up to 100 bar (tip) for high-pressure applications
Signal conditioner | Uses IQS900 signal conditioner. IQS900 has optional diagnostics (built-in test equipment (BITE)), required for SIL 2.
Signal transmission | Up to 1000 m (IQS900 configured with current output)
TQ9xx / IQS900 series

## Slide 18: Proximity measurement chains overview
Comprehensive radial vibration, axial position, rotational speed and phase reference (1/ REV pulse) measurement solutions

## Slide 19: Air gap

## Slide 20: Air gap sensor measurement chains
Key features and benefits
Contactless measurement: No wear-out
Measurement ranges: 30 or 60 mm versions
Three voltage output signals: Pole profile, Rotor profile and Minimum gap (suitable for direct protection)
One current output signal: Configurable as one of Pole profile, Rotor profile or Minimum gap
Easy, fast and reliable installation
Enhanced filtering of noise and spikes induced by high excitation currents
Electric field (capacitance) technology for the contactless measurement of air gap (rotor and stator) in hydroelectric generators and other large machines
LS12x / ILS73x series

## Slide 21: Housing expansion probes

## Slide 22: Housing expansion probes
Key features and benefits
Contactless measurement: No wear-out
Measurement ranges: 50 or 100 mm versions
Integrated electronics: Current output signal
Splash proof: IP54 protection rating
AE119
Eddy-current technology for the contactless measurement of absolute housing expansion on medium to large thermal machines such as gas turbines and steam turbines

## Slide 23: Thank you

## Slide 24: Disclaimer
Business legal entity, Business address
Legal entity registration information as appropriate
Information contained in this document may be subject to export control regulations of the United Kingdom, European Union, United States or other national jurisdictions, including the US International Traffic in Arms Regulations and/or Export Administration Regulations.
Each recipient of this document is responsible for ensuring that transfer or use of any information contained herein complies with all relevant Export Control Regulations.
Copyright © 2022 Meggitt SA. All rights reserved.