## Slide 1: Hardware Solutions
  Presenter:
Title:
Date:

## Slide 2
Advanced systems for machinery protection and condition monitoring specially designed for critical rotating machinery within the power generation, oil & gas, and process industries.
Notes: Product line logic
Add real examples of application (number of VM600 installed etc)

## Slide 3: Product lines overview
  Advanced machinery protection and condition monitoring software
Software
  Protection and Monitoring system for critical rotating machinery
Hardware
Sensing solutions to monitor critical plant and equipment
Sensors & Conditioners
Notes: Customer centric, small and agile,
We offer tailored made and competitive products, solutions and services to our customers,
We deliver differentiated protection and condition monitoring solutions with highly demanding requirements to the power generation industry and other adjacent markets

## Slide 4
Portfolio overview

## Slide 5
Overspeed
protection system
HARDWARE PORTFOLIO OVERVIEW advanced machinery protection, condition and performance monitoring for high value critical machinery
Protection & condition monitoring
VM600Mk2 rack-based advanced machinery protection and condition monitoring system.
* 1U and 6U format
VibroSmart transmitter-based scalable system suitable for both smaller and larger rotating machinery
SpeedSys300 Scalable, robust and independent layer of protection to deliver fast and reliable protection for speed and acceleration.
Notes: Product line logic
Add real examples of application (number of VM600 installed etc)

## Slide 6: Protection & condition monitoring
Rack-based solutions

## Slide 7: VM600Mk2
6U
1U
Formats

## Slide 8: DESIGN CONCEPT
VM600Mk2
Centralized system designed to centrally process a wide range of dynamic inputs coming from a large variety of critical assets.
Flexible network architecture easy integration with VibroSmart distributed monitoring system for optimal and flexible network architecture in a condition monitoring system platform.
All measurements in one card enables complex systems to be built with a minimum number of cards through the well thought modular structure and smart function combination.
MPCMk2 protection module with integrated condition monitoring capabilities
Industry standards
    API 670 fully compliant
    Cybersecurity certification per IEC62443
    SIL 2

## Slide 9
VM600 success story
Over 8’000 VM600 racks produced and installed worldwide
5’500 CMC16/XMV16/XMC16 condition monitoring modules
40’000 MPC4 machinery protection modules
20 years of field experience: VM600 was introduced to market in 2001
Innovative drive: VM600Mk2 is vibro-meter latest rack-based system for protection and condition monitoring

## Slide 10: MPC4Mk2 + IOC4Mk2
4 dynamic input channels + 2 tacho/aux input channels
4 configurable relays + 1 card fault relay
6 BNC raw outputs
4 analogue outputs (current/voltage)
2 front panel buttons for:
    Card lock
    Card reboot
    Firmware recovery
Ethernet port for communication with VibroSight
    Configuration
    Data visualization
VME bus communication with CPU card
VM600Mk2 Machinery protection system

## Slide 11: New approach with enhanced monitoring capabilities
MPC4
VibroSight condition monitoring software
VM600 rack
Machinery protection
Condition monitoring
Permanent Ethernet communication link
Sensors
Machinery protection configuration software
XMV16
Visibility of relay status, protection alarms and processing results from the monitoring software
Enhanced monitoring capabilities
Change of machinery protection setup requires phisical access to the VM600 rack
Cyber Secure
VM600Mk2 Machinery projection system

## Slide 12: MPC4Mk2 comparison against Mk1
MPC4Mk2 comparison against Mk1 | MPC4 Mk2 | MPC4 Mk1
ADC resolution | 24 bits | 12 bits
Bandwidth | 20 kHz | 10 kHz
Measurement outputs per channel | Up to 5 | Up to 2
Waveforms and spectra for troubleshooting | Yes | No
Epoxy sealed relays with all contacts available | Yes (4 + 1) | No (4)
NO/NC contact and Normally Energized or NDE without jumper configuration | Yes | No
Physical card lock for cyber security | Yes | No
Condition monitoring | Yes (Q3 2021) | No
SIL2 | Yes, by design (2022) | Yes, by experience
VM600Mk2 Machinery projection system

## Slide 13: Single channel procession functions
MPS SW processing name | VibroSight Protect® equivalent | 
(BBAB) Broad Band Absolute Bearing Vibration | Bearing absolute vibration | 
(NB) Narrow Band (Tracking) Vibration | Bearing absolute vibration or Shaft Relative Vibration | 
(RS) Relative Shaft Vibration | Shaft Relative Vibration | 
(PS) Position | Position Shaft axial position (collar) Shaft axial position (shaft end) | Rotor position (collar) Differential expansion (collar) Rotor expansion (collar)
(EC) Eccentricity | Shaft eccentricity | 
(HE) Absolute Housing Expansion | Housing expansion | 
(SEP) Relative Shaft Expansion With Pendulum | Differential expansion (pendulum) or Rotor expansion (pendulum) | 
(BBP) Broad Band Pressure | Broad band pressure | 
(QSP) Quasi-static Pressure | Quasi-static pressure | 
(QST) Quasi-static Temperature | Quasi-static temperature | 
(NBFS) Narrow Band Fixed Frequency | Bearing absolute vibration or Shaft Relative Vibration | 
Speed | Speed | 
VM600Mk2 Machinery projection system

## Slide 14: RLC16Mk2 for additional relays
VM600Mk2 Machinery projection system
RLC16 Mk2 comparison against Mk1 | RLC16 Mk2 | RLC16 Mk1
Machinery protection relays | 16 | 16
Epoxy sealed relays with all contacts available | Yes | No
NO/NC contact and Normally Energized or NDE without jumper configuration | Yes | No
Card OK raw bus output line | Yes | No
Switch all relays to safe state when a module failure is detected | Yes | No
SIL2 | Yes, by design (2022) | Yes, by experience

## Slide 15: CPUMk2 + IOCMk2 central processing unit
  Communication with MPC4Mk2
  Profibus DP and Modbus TCP interfaces (Modbus RTU not available currently)
  Future Profinet communication protocol will be supported
  Configuration via VibroSight Protect software
  Designed for combustion monitoring applications
  Can disable VME bus communication for collocation of more than 1 card in rack
VM600Mk2 Machinery protection system
Notes: Start selling more of the CPUR and CPUR2 cards as an alternative to CPUM

## Slide 16: VibroSight Protect Software
New easy to use and intuitive user interface
Fast configuration
Checks overall rack configuration consistency (as opposed to one-by-one card configuration)
Machinery protection configuration software

## Slide 17: Dual channel procession functions
MPS SW processing name | VibroSight Protect® equivalent
(SMAX) Smax | X-Y shaft relative vibration
(DHE) Differential Housing Expansion | Differential housing expansion
(RST) Relative Shaft Expansion (shaft taper) | Rotor expansion (single taper) Rotor expansion (dual taper) Differential expansion (single taper) Differential expansion (dual taper)
(RSC) Relative Shaft Expansion (shaft collar) | Shaft axial position (collar) Shaft axial position (shaft end) Rotor expansion (collar) Differential expansion (collar)
(DMF) Dual Mathematical Function | Mathematical function
(DQSP) Delta Quasi-static Pressure | Delta Quasi-static Pressure
(DQST) Delta Quasi-static Temperature | Delta Quasi-static Temperature
(AS) Absolute Shaft Vibration | Shaft absolute vibration
VM600Mk2 Machinery projection system

## Slide 18
Extended condition monitoring module XMV16 + XIO16
VM600Mk2 condition monitoring system
For vibration condition monitoring
16 dynamic channels and 4 tachometer (speed) channels, all of which are independently configurable.
Synchronous and seamless data acquisition on all channels
Up to 20 signal extractions per channel
High-resolution FFT up to 6400 lines every 500ms (100ms updater rate possible with lower spectral resolution)
Order Tracking
Direct gigabit Ethernet communication » Hardware is fully software configurable
Highly suitable for vibration monitoring for critical and large industrial applications.

## Slide 19
Condition monitoring modules XMC16 + XIO16
VM600Mk2 condition monitoring system
For combustion and vibration monitoring
Specific FFT windows options
Proprietary algorithm included (OEM application)
Provides 16 dynamic channels and 4 tachometer (speed) channels, all of which are independently configurable.
Synchronous and seamless data acquisition on all channels
Up to 20 signal extractions per channel (Band-Peak extraction for Combustion Monitoring)
High-resolution FFT up to 6400 lines every 500ms (100ms updater rate possible with lower spectral resolution)
Order Tracking (New feature !!!)
Direct gigabit Ethernet communication » Hardware is fully software configurable

## Slide 20
Rack controller and communication interface module CPUMk2 + IOCMk2
VM600Mk2 condition monitoring system
System controller and data communication gateway for VM600Mk2 systems.
Industry standard fieldbus communications interfaces: Modbus TCP and PROFIBUS DP.
Mathematical operations on fieldbus data.
System status (health) information available via fieldbus.
Front-panel alarm reset (AR) button.
VM600 rack (CPUMk2) security with a removable key.
Available modules
CPUMk2 + IOCMk2 module for Modbus RTU/TCP

## Slide 21
Key Features
User-friendly advanced vibration monitoring and analysis
Allows to efficiently handle large numbers of measurement points and extensive volumes of data
Easy collection of data from multiple different systems is supported in cyber secure environments
VibroSight suite
VM600Mk2 condition monitoring system
Modular, flexible and comprehensive machinery protection and condition monitoring solutions for a wide range of applications within the power generation, oil & gas, and process industries.

## Slide 22: Distributed monitoring system
VibroSmart VSV301

## Slide 23: DESIGN CONCEPT
VibroSmart VSV301
Flexible Highly scalable and easy to extend
Wide range of applications From stand-alone unit on balance of plant equipment, up to several connected units for larger critical rotating machinery.
ATEX-certified (Zone 2)
Real time communication Via Ethernet or fieldbus
Lower installation cost Skid-mounting components near to machine
Industry standards
    API 670 fully compliant
    Cybersecurity certification per IEC62443
    SIL 2

## Slide 24: SYSTEM FEATURES
VibroSmart
ATEX-certified (Zone 2)
Directly mounted to the machine (DIN-rail)
Measurement chain: suitable for accelerometers, proximity (eddy current) and velocity sensors.
VibroSight: compatible with vibro-meter’s analysis and data processing software
2 dynamic channels and 1 analog input
Auxiliary input channel for tachometer
4 basic and 2 advanced logic functions to drive the module’s relays
Ethernet communications

## Slide 25: Overspeed protection system
Modular solution

## Slide 27: Design concept
SpeedSys300 is designed as an independent layer of protection; to be fundamentally simple and robust. It delivers fast and reliable protection for speed and acceleration and complies to all industry standards including SIL and ATEX.

## Slide 28: SpeedSys300 ODS301
Key Benefits
Safety by design
Scalable
API 670 Compliant
SIL certified «by design», for SIL2 and SIL3
10+ Years PTI
Built-in diagnostics
Overspeed dedicated system (segregation)
Fast response time
Voting logic
Modular
Suitable for Ex-areas
Compatible with industry standard speed sensors

## Slide 29: Key features
SpeedSys300
SpeedSys300 module key features | 
Sensor compatibility | Proximity (eddy current), electronic (Hall-effect) or magnetic (variable reluctance) speed measurement chains
Signal processing | The ODS301 counts measurement chain pulses and converts them to rotational speed and acceleration measurements, which are compared against configured alarm limits. Safety outputs are activated for critical alarms while non-safety outputs are used for other alarms/status information
Frequency range | 0.025 Hz to 35 kHz
Response time | 10 ms (typical)
Safety outputs | 2 × double-pole single-throw (DPST) safety relays and 1 × analogue 4 to 20mA current loop – certified for SIL safety loops
Non-safety outputs | 2 × single-pole single-throw (SPST) relays, 1 × frequency (speed) output, 1 × binary (status) output and 1 ×Modbus RTU serial interface (read only)
Diagnostics technology | Advanced self-monitoring and diagnostics (that is, built-in self-test (BIST)) monitors and reports the health/status of the complete system
Proof test interval | 10 years (typical)

## Slide 30: SIL 3 configurations
SpeedSys300
PCS/ACTUATOR
SPEED SIGNAL
SPEED SIGNAL
SPEED SIGNAL
PCS/ACTUATOR
SPEED SIGNAL
SPEED SIGNAL

## Slide 31: SIL 2 and analog configurations
SpeedSys300
PCS/ACTUATOR
SPEED SIGNAL
SPEED SIGNAL
PCS/ACTUATOR
SPEED SIGNAL
PCS/ACTUATOR
SPEED SIGNAL

## Slide 32: SpeedSys300 ODS301
  (2-wire with self-monitoring technology), e.g. Meggitt IQS 450 and TQ40x type more info here
  Wide speed range
  Long distance signal transmission (1000 meters)
  Operation up to 180°C
  Preferred solution for a wide range of applications
  (3-wire)
  Easily transmittable and processable digital output
  Less vulnerable to EMI
  Preferred for low rpm / zero speed
  (2-wire)
  Suitable for high temperature applications (300°C)
  Self-powered
  Preferred for high rpm
  Eddy-current
  Electronic hall effect
  Electromagnetic
Sensor input compatibility

## Slide 33: Thank you